## Slide 1: Automated Application-Optimal Battery System Design
Levels of Freedom in Layouting Battery System Configurations
Cell block
Number of cells in a row: CR
Number of rows: CN
Cell
Y
X

## Slide 2: Automated Application-Optimal Battery System Design
Levels of Freedom in Layouting Battery System Configurations
Module
Number of Cell Blocks in a
row: MR
Number of rows: MN
Y
X
Cell Block

## Slide 3: Automated Application-Optimal Battery System Design
Levels of Freedom in Layouting Battery System Configurations
String
Number of Modules in a
row: SR
Number of rows: SN
Y
X
Module
Z

## Slide 4: Automated Application-Optimal Battery System Design
Levels of Freedom in Layouting Battery System Configurations
Pack
Number of Strings in a
row: PR
Number of rows: PN
Y
X
String
Number of
Layers: PL
Z

## Slide 5: Automated Application-Optimal Battery System Design
Integration: Introduction of Inevitable Overhead
  Introduction of the overhead factors 𝑂
  Overhead factors describe additional weight and volume caused by the cooling system, busbars, contactors, …
  Defining system dimensions:
      Pack width:
      Pack length:
      Pack height:
      Pack volume:

## Slide 6: Automated Application-Optimal Battery System Design
Defining the Optimization Problem
Defining the optimization problem:
with
as required capacity and voltage and
as maximal width, length and height

## Slide 7: Automated Application-Optimal Battery System Design
Possible ways to solve the Optimization Problem
  An optimization algorithm generating more than one valid solution is needed
  Evolutional algorithm could also solve these kind of integer optimization programs, but with a lot of overhead for smaller battery systems
  The computation cost of the backtracking algorithm increases with O(z5), where z is the maximum search depth (max parameter value)
  Defining maximum values for the parameters at the beginning would reduce the computation cost
  The parameter sets related to the parallel or the series connection can be considered as separate optimization program

## Slide 8: Automated Application-Optimal Battery System Design
Modified Backtracking
Solving optimization problem with a modified backtracking algorithm:
Example for capacity
Root
PL 1 2 3 …
PN 1 2 3 …
PR 1 2 3 …
CN 1 2 3 …
CR 1 2 3 …
CN 1 2 3 …
CR 1 2 3 … 44 Req. Capacity reached
…
Each time the requirements are fulfilled, the actual
parameter set is saved, and a new parameter set is
searched in next branch.
The backtracking algorithm is only applied to obtain
all parameter sets that fulfill the voltage and capacity
requirements.

## Slide 9: Automated Application-Optimal Battery System Design
Permutation
  The number of iterations required to find all combinations of parameters that satisfy the requirement (capacitance or voltage) and act as lower bounds can be reduced by using permutations
  Example for the capacity:
      Tuple (10,1,1,1,1) fulfills the capacity requirements then (1,10,1,1,1),(1,1,10,1,1),(1,1,1,10,1) and (1,1,1,1,10) also fulfills the requirements
      The permutation induces a symmetry in the parameter space
      Hence all solution for optimization problem can be found by determining the solution on one side of one of the symmetric axis and use the permutation on them
      Moreover, the highest parameter minus one in the lower branch is the upper bound of the parameter of the next branch
(10,1,1,1,1)
(5,2,1,1,1)
(4,3,1,1,1)
(3,2,2,1,1)
(2,2,2,2,1)
(…)
(…)
(…)
(1,10,1,1,1)
(2,5,1,1,1)
(3,4,1,1,1)
(2,3,2,1,1)
(2,2,2,1,2)
(1,1,10,1,1)
(2,1,5,1,1)
(3,1,4,1,1)
(2,2,3,1,1)
(2,2,1,2,2)
(1,1,1,10,1)
(2,1,1,5,1)
(3,1,1,4,1)
(2,2,1,3,1)
(2,1,2,2,2)
(1,10,1,1,10)
(2,1,1,5,5)
(3,1,1,1,4)
(2,2,1,1,3)
(1,2,2,2,2)

## Slide 10: Automated Application-Optimal Battery System Design
Ranking of the solutions
  Filter & Sorting
      The list of parameter sets found by the backtracking algorithm is reduced by applying filters to the list. The filters represent the conditions acting as upper limit
      After all parameter sets are filtered and therefore fulfilling all conditions, the list of parameter sets is sorted by the volume

## Slide 11: Automated Application-Optimal Battery System Design
Parallel & Series Connection
  Parallel connection
      The parallel connection of string and cells should be always possible and therefore it should not cause any problems
  Series connection
      For a series connection of neighboring modules in a string or neighboring cell blocks in a module, a chain with certain start and end points (terminals) is searched for
      The existence of such chain depends on the number of modules/cell blocks and their arrangement and cannot be guaranteed

## Slide 12: Automated Application-Optimal Battery System Design
Basic Battery Model Interdependencies
SOC(tn)
TBAT(tn)
SOHC(tn)
I(tn+1)
SOC-Model
SOHR(tn)
T-Model
SOHC -Model
SOHR -Model

## Slide 13: Automated Application-Optimal Battery System Design
Levels of Freedom in Layouting Battery System Configurations
Cell block
Cell
Y
X
Cell block

## Slide 14: Automated Application-Optimal Battery System Design
Cell block
Module
Levels of Freedom in Layouting Battery System Configurations
Module
Y
X

## Slide 15: Automated Application-Optimal Battery System Design
Levels of Freedom in Layouting Battery System Configurations
String
Z
Module
String
Y
X

## Slide 16: Automated Application-Optimal Battery System Design
Levels of Freedom in Layouting Battery System Configurations
Pack
Z
String
Pack
Y
X